## Slide 2: Commercializing the Industrial Beet-Sugar Pathway in the Northern Plains
David Ripplinger
January 31, 2014
Notes: Good afternoon.
My name is David Ripplinger.
I’m a bioenergy economist at NDSU.
My primary job is to work with industry and farmers to develop new bioenergy projects and ensure the viability of existing ones.
My background is in agriculture, but in my job I’ve had to become acquainted with energy. In many ways energy dominates my work. It is very big industry and changes in energy markets move ag markets.
The issue of energy is important to my work in two ways. First, many bioenergy projects require a lot of energy – so I need to be concerned with energy as an input. At the same time, many of the products produced compete directly with existing ones made using petroleum. This includes motor fuels, heating fuels, and plastics.

## Slide 3: The General Idea
Sugar is
Nature’s store of easily
accessible energy
Readily convertible into a number of fuels and products
Beets are an economical way of producing sugar
Breed/engineer for sugar quantity not quality

## Slide 4: Industrial Beets Defined
Aka energy beets
Varieties of beta vulgaris bred to maximize fermentable sugar
May not meet quality standards for food production (sugar beet)

## Slide 5: The European Experience

## Slide 6: Region- Specific Energy Beet Supply Chains
Beets grow well in many agroecosystems
Supply chains will differ because of climate
Considerations
Economics
Energy use
Land use change
Environmental impacts

## Slide 7: Spring Beets
-Planted in the Spring harvested in the Fall
-Dryland or irrigated production
-May be stored outdoors over winter in colder climates
Example: North Dakota
Rotation: Corn/Soybeans/Small Grain/Beets
Long days, cool nights put on sugar

## Slide 8: Winter Beets
Planted in the fall
harvested in the spring
Grown in areas where
hard freezes are unlikely
Dryland production
Example: Mississippi Delta
No land use impacts

## Slide 9: Just in Time Beets
Planted and harvested throughout the year
Irrigated
Example: San Joaquin Valley
Rotation: alfalfa/beans/sunflower/melons/wheat/beets

## Slide 10: Designing a northern Industrial beet-sugar system

## Slide 11
Initial feasibility
Research: yield trials, burn tests and juice storage
Phase 1
Initial Research
Phase 2
Current Research
Phase 3
Commercialization
Research: yield trials, front-end processing, juice storage
Developing federal crop insurance program
Advanced biofuel petition with EPA
2014-2016: finalize processing & commercialization strategies – including feedstock commitments and capitalization
2015 or 2016: First crop grown and facility built

## Slide 12
Project Partners
Department of Agribusiness & Applied Economics
Department of Agriculture and Biosystems Engineering
Plus support from many North Dakota communities and grant funding from APUC and ND Renewable Energy Council
5

## Slide 13: NDSU Research
“Phase II”
Front-end
Whole beet
Juice
Field trials
Crop insurance
Economic and environmental

## Slide 14: Front-End Processing
Hammer mill
Chamber filter press
Modified ribbon mixer with hot water spray
Juice for biofuel
Pulp for pellets
Beets
Beet to juice and pulp
+

## Slide 15: Beet/Juice Storage

## Slide 17
2009-2013 North Dakota Industrial Beet Trials
Chart: Tons Per Acre
| Oakes Irr - DICKEY (A) | Dazey Irr - GRIGGS (B) | Dazey Dry -GRIGGS (B) | Carrington Irr - FOSTER (C) | Carrington Dry - FOSTER (C) | Turtle Lake Irr - McLEAN (D) | Williston Irr - WILLIAMS (E) | Minot Dry - WARD-(F) | Langdon Dry -CAVALIER (G) | Spiritwood Dry - STUTSMAN (H) | Litchville Dry - BARNES (I) | Harvey Dry- WELLS (J) | Colgate Dry - STEELE (K)
2009 | 25.8 | 23.9 | 23.4
2010 | 37.4 | 35.5 | 31.7 | 37.8 | 25.2 | 25.9 | 31
2011 | 34.5 | 27.1 | 25.9 | 25.2 | 25 | 25.3 | 24.8 | 27.8 | 26.5
2012 | 44.4 | 39.7 | 31.2 | 21.4 | 36.2 | 29.4 | 23.8 | 31.3 | 20 | 33.2 | 29.1 | 22.9
2013 | 30.6 | 43.9 | 14.5 | 28.1 | 23.6 | 37.6 | 33.4 | 29.1 | 16.2 | 25.5 | 29.5
2013 notes: Dazey dryland trial had severe herbicide carryover injury. Litchville trial was placed on saline site.

## Slide 18
2009-2013 North Dakota Industrial Beet Trials
Chart: Sugar Content
| Oakes Irr - DICKEY (A) | Dazey Irr - GRIGGS (B) | Dazey Dry -GRIGGS (B) | Carrington Irr - FOSTER (C) | Carrington Dry - FOSTER (C) | Turtle Lake Irr - McLEAN (D) | Williston Irr - WILLIAMS (E) | Minot Dry - WARD-(F) | Langdon Dry -CAVALIER (G) | Spiritwood Dry - STUTSMAN (H) | Litchville Dry - BARNES (I) | Harvey Dry- WELLS (J) | Colgate Dry - STEELE (K)
2009 | 16.2 | 15 | 16.3
2010 | 17.8 | 18.3 | 16.8 | 18.5 | 19.2 | 18 | 17.7
2011 | 16.9 | 20 | 18.8 | 17.3 | 17.4 | 19.7 | 16.4 | 19.1 | 20.7
2012 | 16.7 | 19.7 | 18.8 | 19.5 | 17.2 | 17.8 | 19.3 | 18.1 | 19.7 | 21.2 | 18.5 | 19.9
2013 | 15.8 | 17.5 | 16.4 | 18.4 | 17.4 | 17.1 | 16.1 | 18.4 | 18.4 | 17.5 | 18.2

## Slide 19: Agronomic Benefits
Deep tap root can improve soil health
Allow beet to endure drought conditions
Provide access to nutrients far below the surface

## Slide 20: Herbicide Carryover
Growers must plan ahead on herbicides two to four years due to potential of carry-over damage to beets
  ALS-inhibiting Group 2 herbicides have rotational restrictions of up to 40 months
  Spartan & products containing sulfentrazone (Atrazine, Sonalan, Treflan, Prowl) have rotational restrictions of 24 months or longer
  Pay attention to pre-mixture herbicides. For example, Extreme contains imazethapyr (Pursuit) so it has 40-month rotational restriction

## Slide 21: Retrospective Returns Per Acre
Chart: 
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
Beet Revenue | 766 | 664 | 582 | 938 | 1102 | 1266 | 800
Beet Expenses | 590.82 | 712.76 | 614.39 | 699.64 | 679.42 | 684.79 | 684.79
Returns to Beet | 175.18 | -48.76 | -32.39 | 238.36 | 422.58 | 581.21 | 115.21
Beet v Corn | -58.61 | -71.84 | 45.62 | -17.97 | 240.61 | 149.05 | 130.21
Source: FINBIN, NDSU

## Slide 22: EPA Petition
Federal policy (RFS) mandates the use of different biofuels by type.
Advanced biofuels, have an environmental footprint half the size of gasoline, and less than corn-ethanol
EPA is charged with verifying new fuels footprints
Notes: Make a comment about the RFS.

## Slide 23
Life cycle assessment completed in 2011 to quantify energy use and greenhouse gas emissions associated with the production of ethanol using beets
A petition for an advanced biofuel designation was submitted by Green Vision Group to EPA in October 2011
Provided supplemental data and documentation in spring 2012

## Slide 24: Siting
Five communities under consideration
Facilities may produce industrial sugar or a finished product like ethanol
Notes: Locations may produce industrial sugar feedstock or a finished product.
Processing facilities may produce:
Industrial sugar feedstock (for third party)
Ethanol
Advanced chemicals

## Slide 25: Feedstock Requirements
20 MMGPY Refinery
Requires about 750,000 tons of beets
30,000 dryland acres (@25t/AC)
120,000 acres with a four-year rotation
Most feedstock sourced within 20 miles of plant
Fewer irrigated acres are needed
25

## Slide 26: Growers are critical Without growers there is no plant

## Slide 27: Summary
Beets show significant promise as an industrial crop
Efforts to commercialize are underway
Growers need to be ready