## Slide 2: Sweet Developments: Commercialization of Energy Beets in North Dakota
David Ripplinger
International Biomass Conference
March 2014
Orlando, Florida
Notes: Good afternoon.
My name is David Ripplinger.
I’m a bioenergy economist at NDSU.
My primary job is to work with industry and farmers to develop new bioenergy projects and ensure the viability of existing ones.
My background is in agriculture, but in my job I’ve had to become acquainted with energy. In many ways energy dominates my work. It is very big industry and changes in energy markets move ag markets.
The issue of energy is important to my work in two ways. First, many bioenergy projects require a lot of energy – so I need to be concerned with energy as an input. At the same time, many of the products produced compete directly with existing ones made using petroleum. This includes motor fuels, heating fuels, and plastics.

## Slide 3: The General Idea
Sugar is
Nature’s store of easily
accessible energy
Readily convertible into a number of fuels and products
Beets are an economical way of producing sugar
Breed/engineer for sugar quantity not quality

## Slide 4: Industrial Beets Defined
Aka energy beets
Varieties of beta vulgaris bred to maximize fermentable sugar
May not meet quality standards for food production (sugar beet)

## Slide 5: Beet Agronomics

## Slide 6: Can you grow beets outside the RRV?

## Slide 7
2009-2013 North Dakota Industrial Beet Trials
Chart: Tons Per Acre
| Oakes Irr - DICKEY (A) | Dazey Irr - GRIGGS (B) | Dazey Dry -GRIGGS (B) | Carrington Irr - FOSTER (C) | Carrington Dry - FOSTER (C) | Turtle Lake Irr - McLEAN (D) | Williston Irr - WILLIAMS (E) | Minot Dry - WARD-(F) | Langdon Dry -CAVALIER (G) | Spiritwood Dry - STUTSMAN (H) | Litchville Dry - BARNES (I) | Harvey Dry- WELLS (J) | Colgate Dry - STEELE (K)
2009 | 25.8 | 23.9 | 23.4
2010 | 37.4 | 35.5 | 31.7 | 37.8 | 25.2 | 25.9 | 31
2011 | 34.5 | 27.1 | 25.9 | 25.2 | 25 | 25.3 | 24.8 | 27.8 | 26.5
2012 | 44.4 | 39.7 | 31.2 | 21.4 | 36.2 | 29.4 | 23.8 | 31.3 | 20 | 33.2 | 29.1 | 22.9
2013 | 30.6 | 43.9 | 14.5 | 28.1 | 23.6 | 37.6 | 33.4 | 29.1 | 16.2 | 25.5 | 29.5
2013 notes: Dazey dryland trial had severe herbicide carryover injury. Litchville trial was placed on saline site.

## Slide 8
2009-2013 North Dakota Industrial Beet Trials
Chart: Sugar Content
| Oakes Irr - DICKEY (A) | Dazey Irr - GRIGGS (B) | Dazey Dry -GRIGGS (B) | Carrington Irr - FOSTER (C) | Carrington Dry - FOSTER (C) | Turtle Lake Irr - McLEAN (D) | Williston Irr - WILLIAMS (E) | Minot Dry - WARD-(F) | Langdon Dry -CAVALIER (G) | Spiritwood Dry - STUTSMAN (H) | Litchville Dry - BARNES (I) | Harvey Dry- WELLS (J) | Colgate Dry - STEELE (K)
2009 | 16.2 | 15 | 16.3
2010 | 17.8 | 18.3 | 16.8 | 18.5 | 19.2 | 18 | 17.7
2011 | 16.9 | 20 | 18.8 | 17.3 | 17.4 | 19.7 | 16.4 | 19.1 | 20.7
2012 | 16.7 | 19.7 | 18.8 | 19.5 | 17.2 | 17.8 | 19.3 | 18.1 | 19.7 | 21.2 | 18.5 | 19.9
2013 | 15.8 | 17.5 | 16.4 | 18.4 | 17.4 | 17.1 | 16.1 | 18.4 | 18.4 | 17.5 | 18.2

## Slide 9: Soil Health, Drought Resistance, Nutrient Use
Deep tap root can improve soil health
Allow beet to endure drought conditions
Provide access to nutrients far below the surface

## Slide 10: Herbicide Carryover
Growers must plan ahead on herbicides two to four years due to potential of carry-over damage to beets
  ALS-inhibiting Group 2 herbicides have rotational restrictions of up to 40 months
  Spartan & products containing sulfentrazone (Atrazine, Sonalan, Treflan, Prowl) have rotational restrictions of 24 months or longer
  Pay attention to pre-mixture herbicides. For example, Extreme contains imazethapyr (Pursuit) so it has 40-month rotational restriction

## Slide 11: Beet Production Economics

## Slide 12: Retrospective Returns Per Acre
Chart: 
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
Beet Revenue | 766 | 664 | 582 | 938 | 1102 | 1266 | 800
Beet Expenses | 590.82 | 712.76 | 614.39 | 699.64 | 679.42 | 684.79 | 684.79
Returns to Beet | 175.18 | -48.76 | -32.39 | 238.36 | 422.58 | 581.21 | 115.21
Beet v Corn | -58.61 | -71.84 | 45.62 | -17.97 | 240.61 | 149.05 | 130.21
Source: FINBIN, NDSU

## Slide 13: Advanced Biofuel Designation

## Slide 14: EPA Petition
Federal policy (RFS) mandates the use of different biofuels by type.
Advanced biofuels, have an environmental footprint half the size of gasoline, and less than corn-ethanol
EPA is charged with verifying new fuels footprints
A petition for beet-ethanol was submitted in October 2011
Notes: Make a comment about the RFS.

## Slide 15: Processing

## Slide 16: Fermentable, not necessarily food-grade sugar

## Slide 17: How many days per year can the plant operate?
Notes: GVG goal is 330-340 days; year-around.
Research to date on whole beet storage has not produced economically viable results.
Therefore, conversion to juice for storage is current plan.

## Slide 18: Beet/Juice Storage

## Slide 20: How can we economically reconfigure the front-end?
Notes: A ‘greenfield’ approach; different than sugar factory.
Minimize energy consumption (for EPA designation).
Reduce costs.
Maximize sugar extraction relative to energy consumed for extraction.

## Slide 21: Front-End Processing
Hammer mill
Chamber filter press
Modified ribbon mixer with hot water spray
Juice for biofuel
Pulp for pellets
Beets
Beet to juice and pulp
+

## Slide 23: Project Development

## Slide 24
Project Development Partners
Department of Agribusiness & Applied Economics
Department of Agriculture and Biosystems Engineering
Plus support from many North Dakota communities and grant funding from APUC and ND Renewable Energy Council
24

## Slide 25: First Site
As soon as 2016
Five communities under consideration
  Cando, Carrington, Langdon, Jamestown, Valley City
Facilities may produce industrial sugar or a finished product like ethanol
Notes: Locations may produce industrial sugar feedstock or a finished product.
Processing facilities may produce:
Industrial sugar feedstock (for third party)
Ethanol
Advanced chemicals

## Slide 26
Initial feasibility
Research: yield trials, burn tests and juice storage
Phase 1
Initial Research
Phase 2
Current Research
Phase 3
Commercialization
Research: yield trials, front-end processing, juice storage
Developing federal crop insurance program
Advanced biofuel petition with EPA
2014-2016: finalize processing & commercialization strategies – including feedstock commitments and capitalization
2015 or 2016: First crop grown and facility built

## Slide 27: Feedstock Requirements
20 MMGPY Refinery
Requires about 750,000 tons of beets
30,000 dryland acres (@25t/AC)
120,000 acres with a four-year rotation
Most feedstock sourced within 20 miles of plant
Fewer irrigated acres are needed
27

## Slide 28: Grower Education Meetings

## Slide 29: Growers are critical Without growers there is no plant

## Slide 30: Summary
Beets show significant promise as an industrial crop
Efforts to commercialize are underway
Growers need to be ready