## Slide 2: The Economics of Biomass Combined Heat & Power
David Ripplinger
Bioenergy Specialist
NDSU Extension
Minnesota Renewable Energy Roundtable
Rochester, MN
July 17, 2015

## Slide 3: CHP Basics
Generating electric power and useful energy from a single fuel source
35% Efficient
70% Efficient
80% Efficient
Notes: Recover otherwise wasted thermal energy to produce useful thermal energy or electric power.

## Slide 4
Chart: Minnesota CHP Facility Count
| Coal | Natural Gas | Oil | Waste | Biomass-boiler | Biomass-microturbine | Biomass-reciprocating engine
 | 8 | 13 | 1 | 3 | 7 | 2 | 9
Source: ICF CHP Database
Chart: Minnesota CHP Capacity (kW)
| Coal | Natural Gas | Oil | Waste | Biomass-boiler | Biomass-microturbine | Biomass-reciprocating engine
 | 238250 | 323865 | 3900 | 63700 | 188500 | 185 | 7532

## Slide 5: CHP Benefits: Economic
Lower cost Less price variability
Chart: Minnesota Electricity Rates, 2001-2015
Source: Energy Information Administration

## Slide 6: CHP Benefits: Efficiency
Recover otherwise wasted thermal energy
Takes place closer to energy consumer- lower losses to transmission & distribution

## Slide 7: CHP Benefits: Environmental
More efficient energy use
Lower carbon fuels
Lower greenhouse gas
emissions!

## Slide 8: CHP Benefits: Resiliency
For those businesses whose operations depend on reliable power
-Adobe Biogas Fuel Cells

## Slide 9: Why Biomass?
Energy cost savings
Greenhouse gas reductions
Local economic development
Reduced supply risk

## Slide 10: When does CHP work best?
High electricity prices
Deregulated electricity markets
Firms with
-Regular operations
-Regular thermal loads
-Existing central plant
-Central plant equipment replacement or major construction planned
-Reliability concerns
-Environment

## Slide 11: Determining Feasibility: The Spark Spread

## Slide 12
-
+
Spark Spread
=

## Slide 13
CHP heat rate (MMBtu/kWh)
CHP fuel price ($/MMBtu)
3,413 MMBtu/kWh
Power-to-heat ratio
Boiler efficiency (%)
Avoided cost of thermal fuel ($/MMBtu)
Avoided cost of power ($/kWh)
.1
x
÷
÷
÷
-
+
Spark Spread
=

## Slide 14
3,413 MMBtu/kWh
$.08/kWh
$6/MMBtu
80%
.1
$5/MMBtu
.0141 MMBtu/kWh
x
$.08/kWh
$.02/kWh
$.0705/kWh
÷
÷
÷
-
+
Spark Spread
=
$.03/kWh =

## Slide 15: You may have a CHP project if
the spark spread is positive
…we didn’t account for
capital costs and O&M.

## Slide 16: Adding the Cost of Capital
Assumptions
Electric Capacity (MW) 3
Annual Operating Hours 8,000
Capital Cost $18,000,000
Calculations
Cost per kW $6,000
Cost of Capital 8%
Cost per kWh $.06
+ O&M from $.02 to $.10+/kWh

## Slide 17: Sensitivity Analysis
Prices: electricity, boiler fuel, CHP fuel, capital, O&M
Technology: boiler efficiency, power to heat ratio, CHP heat rate
Project scale and scope
Alternative fuels

## Slide 18: What about risk?
Price risk
Supply risk
Policy risk
Operating risk

## Slide 19: What about emissions?
Calculate the spark spread using carbon instead of financial accounting
Price using a carbon price (eg $20 MT/CO2e)

## Slide 20
Avoided GHG emissions of power
(g CO2 e/kWh)
Avoided GHG emissions of thermal fuel
(g CO2 e/MMBtu)
Boiler efficiency (%)
Power-to-heat ratio
÷
÷
3,413 MMBtu/kWh
÷
CHP GHG emissions
(g CO2 e/MMBtu)
CHP heat rate (MMBtu/kWh)
x
-
+
Green
Spark Spread
=

## Slide 21: !
Someone needs to get EPA better biomass carbon emissions values for their CHP emissions calculator ASAP!

## Slide 22: CHP Policy
Federal
  Tax Incentives
  Financing (§1703)
  Boiler MACT
  §111(d)
State
  Next Generation Energy Act (MN)
  RPS
  CIP
  Net metering
  Standby
  Incentives/financing

## Slide 23: Summary
Know the basics
Calculate the spark
Follow policy developments

## Slide 24
David Ripplinger
Bioenergy Specialist
david.ripplinger@ndsu.edu
701.231.5265